## Slide 1: Project: Learning Exploration via Reinforcement Learning
Agent’s exploration framework is split into 3 distinct processes:
Decision Module (Goal Planning) - FCQN
Planning Module (Path Finding) - RRT n *
SLAM (Simultaneous Localization and Mapping) - 2D LiDAR with BHM
Reference: Haoran Li, Qichao Zhang, Dongbin Zhao, " Deep reinforcement learning based automatic exploration for navigation in unknown environment", IEEE Transactions on Neural Networks and Learning Systems
Adapted from Donovan Loh (Intern)
Notes: Rapidly-Exploring Random Tree Star - path planning algorithim

## Slide 2
3 Channels – Occupancy map, Current position, Previous Positions
Convolutional and Max Pooling Layers
2D training environment
Bayesian Hilbert Maps (BHM) for Occupancy Mapping
Notes: State function V - measures how good it is to be in a particular state
Advantage function - relative measure of the importance of each action
Q-value - the value of choosing a particular action in this state

## Slide 3: Recurrent Neural Networks
An unrolled RNN cell
An unrolled LSTM (Long Short Term Memory) Cell
DRQN (Deep Recurrent Q Network) Architecture (Used on Atari Games)
Reference: Matthew Hausknecht, Peter Stone, "Deep Recurrent Q-Learning for Partially Observable MDPs”, https://arxiv.org/abs/1507.06527
https://colah.github.io/posts/2015-08-Understanding-LSTMs/

## Slide 4
LSTM
LSTM
Q-Values
Q-Values
State St
State St-1
Hidden State Ct
Ct-1
Ct+1
Initial Hidden State Ct=0 - learned at the start of each episode

## Slide 5: Training and Inference Details
Training:
6000 iterations
Original model learning rate = 2x10^-6
New model learning rate = 1x10^-6 (seems to be more stable)
Inference:
Same 7 Valid starting points - 5 episodes per starting point (35 episodes total)
Minimum Exploration rate of 0.77 for each completed episode

## Slide 6: Inference Results
Metric | Original Model | Model (with LSTM layer)
Average Path Length | 2440 | 1520
Average Explored Region Rate | 0.775 | 0.777
Average Exploration Efficiency (Relative Entropy reduced per unit length) | 4.25 | 6.68
Original model - drone gets “stuck” easily (cannot find remaining unexplored region)
LSTM layer seems to reduce this likelihood
Model with LSTM layer produces more “invalid” goalpoints